First drafted by Rich Rudman on 3-2-2002

First rewrite by Joe on 3-3-2002

Assumptions:

These instructions assume that the Mk 2 regulators are removed from the vehicle. You do not need to remove them from the car, but they should be disconnected from the battery pack during installation of the reg bus board.

Warnings:

Battery box connections and charger connections are hot to ground when the charger is plugged into an AC outlet. Disconnect the charger from line power before working on the Reg bus.

Battery packs may have high voltages present with no means to disconnect them. Use appropriate safety practices when working around battery packs.

To prevent burns from dropped tools, use insulated tools when working around batteries.

We cannot be responsible for unsafe or dangerous work habits. If you are unsure of what you are doing or don’t have the right tools to do the job safely, be safe and have a qualified person do the job for you.

Installation:

Plug the Reg bus card onto the MK2 Rudman Regulator using the 3 plastic .500 standoffs. Mate the Samtec BSW connector first, then snap the standoffs through the holes.

Connect the Reg bus boards together with 6 pin RJ phone cable in daisy chain fashion.

Connect one of the end Reg bus boards to a PFC-20 charger with a 6 pin RJ phone cable.

Reg check out.

Set the PFC20 to minimum current.

Turn on the PFC20.

Set DIP switch position 6 to the ON position in the PFC20. This turns on the Equalize mode on the Reg bus. It also turns on the yellow LED on the Reg bus card. This proves that you that the charger can talk to all the Regs and put them into equalize mode. If an LED does not come on, troubleshoot to find the bad connection or part.

Set DIP switch position 3 ON and position 4 off in the PFC20. This connects the hot reg warning signal to the charge termination timer. Position 4 is a memory switch. If it is on, the charger will need to have the power cycled to get the blue LED to stop blinking. If the switch is off, the LED will stop blinking when the short is removed.

Make sure the blue LED is not blinking. If it is then turn off DIP switch positions 1 and 2.

Momentarily short RT1 on each Reg bus board to simulate a HOT reg condition. This should cause the blue timer timing LED to blink on the PFC20. This should be done as every Reg bus is installed.

Installing a 10K NTC (Negative Temp Coefficient) thermistor to the 2 pin header marked RT1 on the Reg buss will allow Analog temp sensing, as well as digital cut off should a Reg heat sink get too hot.

Connect the Mk 2 regulators to their respective batteries.

Momentarily short the temp sensor (RT1) under the heat sink. This will also simulate a hot reg condition. This action should also cause the blue timer LED to flash.

Conclusion of testing:

Set DIP switch position 1 ON if you are using the voltage regulation time out to shut off the charger at the end of the charge cycle. If you leave this switch off, then the charger will not time out after the battery has sat at acceptance voltage for a fixed period of time.

Set DIP switch position 2 ON if you are using the timer to limit the total charge time. Otherwise leave it OFF.

Set DIP switch position 4 OFF if you are using Digital feedback on the Reg bus and have no RT2 on the Reg bus boards. If you have RT2 on the Regbus boards, then leave it ON.

These check out steps should allow you to install and verify all Reg bus functions expected to work during the charge cycle. Low Battery detect is installed on the boards but the test method has not been finalized.

References:

Wiring: use 6 conductor RJ wire and connectors. The top 5 conductors are used.

1 	White	+5 volts from 78L05 in charger.

2	Black	Hot Reg wire. Hottest regulator controls the voltage on this wire.

3	Red	On charge: pulled low to set regulator threshold up 10% (15.0 to 16.5 typical)

On discharge: pulled low to indicated a battery has gone under the UV setpoint.

4	Green	GND from charger

5	Yellow	Cold reg wire. Coldest regulator controls the voltage on this wire.

6	Blue	Not used.

Make sure all conductors on the Cable go to the same pins on each end of the cable. So that all cables are the same end for end.

100 foot Maximum total cable length.

64 Maximum Reg Bus boards per charger.

Operational notes and ideas.

The sensor on the MK2 Reg is its own temp cutout protection. It will shut off the Reg’s bypass if the heatsink gets to over 190 Deg F.

The Sensor RT1 on the Reg Bus can be attached to the Reg’s heatsink. This gives analog temp regulation of the Reg’s actions. You can then adjust how hot you want a Reg to get from the Setpot inside your PFC20 Charger. This concept can be modified by placing the temp sensor anywhere that you need to have protected from a Reg’s bypass heat. If  you have a Loadless Reg attach the sensor to the remote  heatsink. If you are using the bypass current to heat the battery, then attach the sensor in such away as to measure the batteries temp. All this time the Reg is protecting itself with it’s own sensor. That’s why there’s one on the MK2 Reg and on the RegBuss Card also.

Attaching the temp sensor to the RT1 header, and letting the sensor hang will of course measure the battery box temp. This lets you use the Regs, and their heatsink to heat the battery box, and regulate the entire box or enclosure.

You can get as creative as you wish. Just keep the thermistor leads from touching any conductive objects.  The sensor is connected to internal charger GND and is electrically hot relative to earth ground.